Town of _____________ – Site Inspection Form

Erosion & Sediment Control

Adapted by PVPC from

2013 SOP#6 developed by Fuss & O’Neill for Central MA Stormwater Coalition

Guidelines

- The inspection shall begin at a low point and work uphill, observing all discharge points, erosion and sediment control features, and any off-site support activities.

- Written and photographic records shall be obtained and included in this report for each site visit.

- The inspector shall always wear personal protective equipment appropriate for the site.

- The inspector shall abide by the contractor’s site-specific safety requirements.

- The inspector has legal authority to enter the site. However, if denied permission to enter the site, the inspector shall not force entry.

General information

| Project name: |  |
| --- | --- |
| Project location: |  |
| Site operator: |  |
| Inspector’s name: |  |
| Inspector's title and qualifications: |  |
| Date of inspection: |  | Date of last inspection: |  |
| Start time: |  | End time: |  |
| Type of Erosion and Sediment Control inspection: Stormwater regulations require inspections to occur before start of construction and either at least once every 7 calendar days or once every 14 calendar days and within 24 hours of a storm event of 0.25 inches or greater |
| Before start of ( construction | 7 calendar day ( inspection | 14 calendar day ( inspection | Within 24 hours ( of a storm event ≥ 0.25 inches |
| Describe the weather conditions at time of inspection: |  |
| Describe the current phase of construction: |  |

Document any of the following issues found on the construction site, and the corrective action(s) required for each.

| Issue | Status | Correction Action Needed |
| --- | --- | --- |
| 1. Have all Erosion and Sediment Control (ESC) features been constructed before initiating other construction activities? | Yes ( No ( |  |
| 2. Is the contractor inspecting and maintaining ESC devices regularly? | Yes ( No ( |  |
| 3. Is existing vegetation maintained on the site as long as possible? | Yes ( No ( |  |
| 4. Is construction staged so as to minimize exposed soil and disturbed areas? | Yes ( No ( |  |
| 5. Are disturbed areas restored as soon as possible after work is completed? | Yes ( No ( |  |
| 6. Is clean water being diverted away from the construction site? | Yes ( No ( |  |
| 7. Are sediment traps and sediment barriers cleaned regularly? | Yes ( No ( |  |
| 8. Are vegetated and wooded buffers protected and left undisturbed? | Yes ( No ( |  |
| 9. Are soils stabilized by mulching and/or seeding when they are exposed for a long time? | Yes ( No ( |  |
| 10. Has vegetation been allowed to establish itself before flows are introduced by channels? | Yes ( No ( |  |
| 11. Is regular, light watering used for dust control? | Yes ( No ( |  |
| 12. Is excessive soil compaction with heavy machinery avoided to the extent possible? | Yes ( No ( |  |
| 13. Are erosion control blankets used when seeding slopes? | Yes ( No ( |  |
| 14. Are trees and vegetation that are to be retained during construction adequately protected? | Yes ( No ( |  |
| 15. Are areas designated off-limits to construction equipment flagged or easily distinguishable? | Yes ( No ( |  |
| 16. If topsoil has been excavated and stockpiled for later use on the project, are stockpiles adequately protected? | Yes ( No ( |  |
| 17. Are temporary slope drains or chutes used to transport water down steep slopes? | Yes ( No ( |  |
| 18. Do all entrances to the storm sewer system have adequate protection? | Yes ( No ( |  |

Attach photos as needed for documentation.

The inspector shall provide the applicant/site operator and the ______________ Planning Board (the stormwater authority) with a copy of this report and notice of the corrective action(s) to be taken.

The applicant/site operator shall promptly correct any portion of the work that does not comply or the applicant will be subject to the bonding provisions or the penalty provisions within the Stormwater Management and Erosion and Sediment Control Bylaw and Regulations.